## Slide 1
Wet tropospheric correction comparison for ERS-2 mission between
GPD V2.0 (FCUP) and GPD V1.1 corrections
The GPD V2.0 correction is referred to as GPD_V2.0 in the following study
The GPD V1.1 correction is referred to as GPD_V1.1
Lionel Zawadzki, Michael Ablain (CLS)

## Slide 2
Introduction:
We will observe and analyse the impact of the new GPD wet troposphere correction V2.0 by comparison to its previous version V1.1 for ERS-2 mission and climate applications
The main differences between the two corrections are described in the corresponding technical note
In order to determine the impact of the new wet troposphere correction in terms of climate applications and temporal scales, we will try in this study to indicate for each impact detected if it’s a positive (+) or a negative (-) impact :
Wet tropospheric correction comparison for ERS-2 mission
No impact detected
Low impact
Significant impact

## Slide 3
ERS-2 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GPD_V2.0 Versus GPD_V1.1
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Global Mean Sea Level
Low impact detected on Global Mean Sea Level trend
0.11 mm/yr on the Global MSL is low.
Temporal evolution of SLA mean calculated globally.

## Slide 4
ERS-2 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GPD_V2.0 Versus GPD_V1.1
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Global Mean Sea Level
No impact detected on Inter annual Signals
The figure below shows the mean difference between the two corrections calculated globally by cycle.

## Slide 5
ERS-2 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GPD_V2.0 Versus GPD_V1.1
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Global Mean Sea Level
No impact detected on Annual and Semi-annual Signals

## Slide 6
ERS-2 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GPD_V2.0 Versus GPD_V1.1
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Low impact detected on a short temporal scale (signals < 2 months):
Crossovers Variance Differences are negative at the beginning of the period, then positive (see figures on next slide) between 0 and 1 cm². It is not possible to assess which correction is the best.
The map of SSH crossovers Variance Differences shows that the improvements are mainly in the Tropical band, but there are degradations at higher latitudes.
Mesoscale

## Slide 7
Mesoscale
Map of Variance differences of Sea Surface Height at crossovers between the GPD_V2.0 and GPD_V1.1 corrections (over all the period):
Improvement near the Equator (-1 to -2 cm²)
Degradations at higher latitudes (+1 cm²)
Temporal evolution of Variance differences of Sea Surface Height at crossovers between two GPD corrections :
Low impact over all the period

## Slide 8
ERS-2 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GPD_V2.0 Versus GPD_V1.1
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Low impact detected on Regional Mean Sea Level
We observe a low impact (~ -0.2 mm/yr) globally, and stronger (-0.3 to -0.4mm/yr) in the Pacific Tropical band : negative in the West Pacific and positive (0.1mm/yr) in the East Pacific
Regional Mean Sea Level

## Slide 9
Regional Mean Sea Level
Map of Sea Level Anomaly differences between two GPD corrections (over all the period)

## Slide 10
ERS-2 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GPD_V2.0 Versus GPD_V1.1
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
At high latitudes, amplitude differences reach 1cm for annual signal (see figures on next slide),
At lower latitudes, the amplitude differences do not exceed 2 mm.
The impact on the phase reaches 10 days locally
It’s not possible to determine which correction is the best one for theses scales
Regional Mean Sea Level
Low impact detected on Annual and Semi-Annual Signals

## Slide 11
Regional Mean Sea Level
Map of Sea Level Anomaly differences amplitude for annual signal
Map of Sea Level Anomaly differences amplitude for semi-annual signal
SLA with GPD_V2.0 amplitude – SLA with GPD_V1.1 amplitude : semi-annual signal
SLA with GPD_V2.0 amplitude – SLA with GPD_V1.1 amplitude : annual signal

## Slide 12
Regional Mean Sea Level
Map of Sea Level Anomaly differences phase for annual signal.
Map of Sea Level Anomaly differences phase for semi-annual signal.
To be noted a phase value equal to 30° corresponds to a period of one month
SLA with GPD_V2.0 phase – SLA with GPD_V1.1 phase : semi-annual signal
SLA with GPD_V2.0 phase – SLA with GPD_V1.1 phase: annual signal

## Slide 13
Map of Mean differences between GPD_V2.0 and GPD_V1.1 (extension period)
On this map we observe clearly differences in the tropical band. Considering a global bias, the impact is about 5mm in this area
Map of Standard deviation differences between GPD_V2.0 and GPD_V1.1 (extension period)
On this map we observe differences up to 5mm
Regional statistics between corrections

## Slide 14
To conclude:
GPD_V2.0 correction extension shows performances equivalent to its previous version.
Performances at crossovers are equivalent and the analysis of MSL shows no degradation nor improvement over this period. The improvements are mainly in the Tropical Band
ERS-2 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GPD_V2.0 Versus GPD_V1.1
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Wet tropospheric correction comparison for ERS-2 mission