## Slide 1
Ionospheric correction comparison for ENVISAT mission between the updated dual frequency release after S-band PTR reversion and the reference dual frequency release
The updated correction is referred to as IONO_FILTR_ITER in the following study
The Reference correction is referred to as IONO_FILTR_ITERCorr
Lionel Zawadzki, Michael Ablain (CLS)

## Slide 2
Introduction:
We will observe and analyse the impact of the updated ionospheric correction IONO_FILTR_ITERCorr for ENVISAT from IsardSat for climate applications. A delta of ionospheric correction has been provided by IsardSat. This delta has been added to the raw RA2 ionosperic correction and an iterative filter has been applied as in the reference product.
We will compare this correction with the reference dual frequency ionospheric correction that has been did not benefit from the S-Band PTR reversion process. It will be referred to as “IONO_FILTR_ITER”.
In order to determine the impact of the new ionospheric correction in terms of climate applications and temporal scales, we will try in this study to indicate for each impact detected if it’s a positive (+) or a negative (-) impact :
Ionospheric correction comparison for ENVISAT mission
No impact detected
Low impact
Significant impact

## Slide 3
Valid points
The analysis shows a significant decrease of the number of valid points in the IONO_FILTR_ITERCorr ionospheric correction (up to 15000/cycle), due to missing data in the delta ionospheric correction.
For consistency reasons, the following analyses are performed on the common valid points
Temporal evolution of number of valid points.

## Slide 4
Envisat |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | IONO_FILTR_ITERCorr Versus IONO_FILTR_ITER
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Global Mean Sea Level
low impact detected on Global Mean Sea Level trend
0.08 mm/yr on the Global MSL is low.
(see figure on next slide)
Temporal evolution of SLA mean calculated globally.

## Slide 5
Envisat |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | IONO_FILTR_ITERCorr Versus IONO_FILTR_ITER
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Global Mean Sea Level
No impact detected on Inter annual Signals
The figure below shows the mean difference between the two corrections calculated globally by cycle.

## Slide 6
Envisat |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | IONO_FILTR_ITERCorr Versus IONO_FILTR_ITER
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Global Mean Sea Level
No impact detected on Annual and Semi-annual Signals

## Slide 7
Envisat |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | IONO_FILTR_ITERCorr Versus IONO_FILTR_ITER
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | -
No impact detected on a short temporal scale (signals < 2 months):
Crossovers Variance Differences are generally positive (see figures on next slide) between 0 and 0.05 cm² : this means that the new IONO_FILTR_ITERCorr correction shows a very low degradation by comparison to the reference correction.
The map of SSH crossovers Variance Differences shows that these not significant degradations are mainly at low latitudes (consistent with the ionospheric signal).
Mesoscale

## Slide 8
Mesoscale
Map of Variance differences of Sea Surface Height at crossovers between the IONO_FILTR_ITERCorr and IONO_FILTR_ITER corrections (over all the period):
Very low degradation (<0.5cm²) at low latitudes
Temporal evolution of Variance differences of Sea Surface Height at crossovers between two ionospheric corrections :
Very low degradation before 2006 (< 5mm²) with IONO_FILTR_ITERCorr

## Slide 9
Envisat |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | IONO_FILTR_ITERCorr Versus IONO_FILTR_ITER
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Low impact detected on Regional Mean Sea Level
We observe a non significant impact (<0.05 mm/yr) on the regional trends in the open ocean and up to 0.2mm/yr at low latitudes where the ionospheric signal is strong.
Regional Mean Sea Level

## Slide 10
Regional Mean Sea Level
Map of Sea Level Anomaly differences between two ionospheric corrections (over all the period)

## Slide 11
Envisat |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | IONO_FILTR_ITERCorr Versus IONO_FILTR_ITER
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
At high latitudes, amplitude differences reach 5mm or -5mm for annual and semi-annual signal (see figures on next slide),
At lower latitudes, where the ionospheric signal is the strongest, the amplitude differences are not significant.
It is not possible to determine which correction is the best one for theses scales.
Regional Mean Sea Level
No significant impact detected on Annual and Semi-Annual Signals

## Slide 12
Regional Mean Sea Level
Map of Sea Level Anomaly differences amplitude for annual signal
Map of Sea Level Anomaly differences amplitude for semi-annual signal
SLA with IONO_FILTR_ITERCorr amplitude – SLA with IONO_FILTR_ITER amplitude : semi-annual signal
SLA with IONO_FILTR_ITERCorr amplitude – SLA with IONO_FILTR_ITER amplitude : annual signal

## Slide 13
Regional Mean Sea Level
Map of Sea Level Anomaly differences phase for annual signal.
Map of Sea Level Anomaly differences phase for semi-annual signal.
To be noted a phase value equal to 30° corresponds to a period of one month
SLA with IONO_FILTR_ITERCorr phase – SLA with IONO_FILTR_ITER phase : semi-annual signal
SLA with IONO_FILTR_ITERCorr phase – SLA with IONO_FILTR_ITER phase: annual signal

## Slide 14
Map of Mean differences between IONO_FILTR_ITERCorr and IONO_FILTR_ITER (whole ENVISAT period)
On this map we observe a global bias and very low differences (<0.1mm) at low latitudes between the two ionospheric corrections
Map of Standard deviation differences between IONO_FILTR_ITERCorr and IONO_FILTR_ITER (whole ENVISATperiod)
On this map we observe low differences (<2mm) mainly at low latitudes where the ionospheric signal is strong
Regional statistics between corrections

## Slide 15
To conclude:
IONO_FILTR_ITERCorr correction shows performances equivalent to its previous version even though a very low degradation has been evaluated at crossovers.
The analysis of MSL shows no degradation nor improvement over the ENVISAT period.
However, the diminution of the number of valid points is significant.
Envisat |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | IONO_FILTR_ITERCorr Versus IONO_FILTR_ITER
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Ionospheric correction comparison for ENVISAT mission